South Wootton Village Hall Asbestos Management Plan

Asbestos management plan

Premises:

South Wootton Village Hall

22 Church Lane

South Wootton

Kings Lynn

PE30 3LJ

Date plan produced: 30 September 2016

Reviewed: September 2017

Date of next review: September 2019

Issued to: Parish Council – Policy Committee   		Signed………………………………

Copied to: Tony Walker – Village Hall Caretaker

Contents

- Introduction

- Responsibilities

- Summary of location of asbestos

- Asbestos risk assessment

- Action plan

- Emergency procedures

- Appendix A: Record of inspections on asbestos containing materials (ACMs)

- Appendix B: Record of contractor’s inspection of register

- Appendix C: Asbestos survey report. WEAAR Ltd – 1st September 2016

Introduction

Asbestos is a microscopic mineral fibre that is so small that it can’t be seen with the naked eye. Once disturbed, fibres can remain in the air for hours. If fibres are inhaled, they can cause serious health hazards which might not become apparent for years.

Note: Asbestos should only be disturbed or maintained by specialist personnel, who will be licensed contractors, working under strictly controlled conditions.

Those responsible (the Parish Council) for any non-domestic premises are required to manage them in respect of any asbestos they may contain. This requires knowing what asbestos containing materials (ACMs) may be present, their location and condition. The simplest way to do this is to have a survey undertaken by a professional.

The contents of your survey are then used to produce a management plan, like this one, to help manage the ongoing condition of and access to any ACMs. This should include regular checking of the condition of the ACMs and controlling any building or repair works to ensure this is not disturbed, except by specialists under controlled circumstances.

Responsibilities

Responsible Person

The responsibility for safety matters within the Village Hall premises is that of the South Wootton Parish Council and the Village Hall Caretaker.

The Parish Council has responsibility for the safety of all individuals using the building. They are responsible for ensuring that all responsibilities detailed below and  any improvements and repairs to the premises are carried out at safely and follow good working practice at all times.

The Parish Council are responsible for safety provisions, including the following:

- Ensuring that all persons are aware of potential hazards and that suitable controls are in place

- Ensuring all safety issues, including accidents and incidents, are reported to the Parish Council/Caretaker and are recorded in the accident book

Operational responsibility							Contact Number

Mrs Tracey Cornwell								01553 671692

Mrs Moira Kirby								01553 671692

Mr Michael Narborough (Assets Chairman)					01553 673660

Mr David Price (PC Chairman)						01553 675807

Mr Tony Walker (Person carrying out monitoring and maintenance)	01553 672828

The Parish Council are responsible for ensuring that this plan is put into effect and to make others aware of it, as necessary. They must also ensure that the plan is reviewed every year.

Summary of location, type and condition of asbestos

See survey for details.

In summary, there is asbestos know to be in the following rooms:

- Male Toilet – Ceiling (Very Low Risk)

- Disables Toilet – Ceiling (Very Low Risk)

- Female Toilet – Ceiling (Very Low Risk)

- Committee Room – Ceiling (Very Low Risk)

- Kitchen Ceiling – (Very Low Risk)

- The detail of this is found in Section 4.0 of the plan.

Asbestos risk management

Hazard: Asbestos containing materials (ACM)

Persons affected: Members, visitors, contractors, suppliers etc

Date of assessment: September 2016 Company conducting assessment: WEAAR Limited

NADS – No Asbestos Detected in Sample			NA – Presumed Not Asbestos (no sample taken)

| Item | Location of ACM | Element | Type | Asbestos type | Condition | Risk level | Action | Inspection frequency |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | South Wootton Village Hall |  | WEAAR 16-M-134 |  |  |  |  |  |
|  | Toilets |  |  |  |  |  |  |  |
| Sample 3 | Male Toilets | Ceiling Panels | Plasterboard/Textured Coating | Chrysotile (White) | Good | Very Low | No further action necessary as present. If damaged, remove by trained operative | Monthly by VH Caretaker |
| As 3 | Disabled Toilet | Ceiling Panels | Plasterboard/Textured Coating | Chrysotile (White) | Good | Very Low | No further action necessary as present. If damaged, remove by trained operative | As above |
| As 3 | Female Toilet | Ceiling panels | Plasterboard/Textured Coating | Chrysotile (White) | Good | Very Low | No further action necessary as present. If damaged, remove by trained operative | As Above |
|  | Committee Room |  |  |  |  |  |  |  |
| As 3 | Committee Room | Ceiling panels | Plasterboard/Textured Coating | Chrysotile (White) | Good | Very Low | No further action necessary as present. If damaged, remove by trained operative | As Above |
|  | Kitchen |  |  |  |  |  |  |  |
| As 3 | Kitchen | Ceiling panels | Plasterboard/Textured Coating | Chrysotile (White) | Good | Very Low | No further action necessary as present. If damaged, remove by trained operative | As Above |
|  | Entrance Ceiling |  |  |  |  |  |  |  |
| Photo 7966 | Entrance Ceiling | Ceiling | Asbestos Insulation Board Panels | NADS | - | - | No Action required | - |
|  | Foyer Ceiling |  |  |  |  |  |  |  |
| Photo 7967 | Foyer Ceiling | Ceiling | Plasterboard/Textured Coating | NADS | - | - | No Action required | - |
|  | Foyer Loft |  |  |  |  |  |  |  |
| Photo 7968 | Foyer Loft | Tiles | Plasterboard/Boarded | NA | - | - | No Action required | - |
|  | Caretaker Cupboard |  |  |  |  |  |  |  |
| AS 02 | Cupboard Ceiling | Ceiling | Plasterboard/Textured Coating | NADS | - | - | No Action required | - |
|  | Main Hall |  |  |  |  |  |  |  |
| Photo 7975 | Main Hall Ceiling | Ceiling | Plasterboard | NA | - | - | No Action required | - |
|  | Cupboard |  |  |  |  |  |  |  |
| Photo 7976 | Cupboard | Ceiling | Plasterboard | NA | - | - | No Action required | - |
|  | Bar |  |  |  |  |  |  |  |
| Photo 7977 | Bar | Ceiling | Plasterboard | NA | - | - | No Action required | - |
|  | Back Storage Area |  |  |  |  |  |  |  |
| Sample 4 | The Cages area | Floor | Solid/Vinyl Tiles | NADS | - | - | No Action required | - |
| Sample 5 | The cages area | Ceiling | Plasterboard/Textured Coating | NADS | - | - | No Action required | - |
|  | Roof Undercloak |  |  |  |  |  |  |  |
| Sample 6 | Roof Undercloak | Undercloak | Insulation Board | NADS | - | - | No Action required | - |

Action plan

Given the condition and location of the asbestos and the use of the buildings, the decision has been taken to, where possible, leave the asbestos in place and manage it to prevent it being disturbed.

The following actions will be taken to manage the asbestos:

This plan will be reviewed annually by the Parish Council in consultation with the Village Hall Caretaker.

The contents of this plan will be explained to key members.  Any visitors, suppliers or contractors will have access to the asbestos management plan. Records will be kept at the back of this plan (Appendix B).

Key adults will be briefed on what action to take if any asbestos is accidently disturbed.

The Parish Council will update the asbestos management plan if any asbestos is removed or treated.

The Parish Council with the Village Hall Caretaker will ensure that no work is undertaken in any part of the building that will disturb asbestos by either staff or contractors.

The condition of any asbestos will be monitored regularly in accordance with the asbestos management plan. If it is found to be damaged or becoming friable, the area will be evacuated until the risks are reassessed and controlled.

The Parish Council will make the asbestos survey report available to anyone who may need to see it.

Any works proposed which will affect the asbestos must first be approved by the Parish Council  after taking advice from a competent person. Contractors carrying out such work will need to be licensed and demonstrate their competence before being allowed to start. A full risk assessment and method statement will need to be produced, including disposal arrangements for the waste.

Any asbestos waste disposed of must be properly documented and copies of consignment notes filed with the Parish Council.  Amendments to the asbestos management plan must be made.

6.0 Emergency procedures

Asbestos Containing Materials (ACM’s)

If damage occurs to any ACM:

- Stop activity or work immediately

- Keep people away from the area

- Inform the Parish Council or the Village Hall Caretaker at the earliest opportunity

- Lock off the affected area

- Put up warning signs to keep people out of the area

- Arrange for a licensed contractor to remove or repair the damage.

If dust or debris gets onto your clothing, wipe down clothing with damp rags, remove any contaminated clothing and place all contaminated items in a sealed bag. Seal the bag, then bag again, and arrange for disposal as contaminated asbestos waste. This must be via a licensed carrier and go to a licensed waste disposal point.

Ensure that an incident report form is completed and the Parish Council/Village Hall Caretaker are informed.

Appendix A

6 Monthly asbestos inspection record. Inspected by................................................................................ on (date).....................................................

This sheet must be completed each time the asbestos containing Material (ACM) is inspected. Any deterioration or damage identified must be brought to the attention of the Parish Council immediately by the person carrying out the inspection.

| Date | Item (see Section 4.0) | Location of ACM | Findings/condition (note any damage/deterioration) | Inspected by | Necessary remedial action | Responsible Person | Date to be completed by | Date completed |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Appendix B

Record of contractors’ inspection of asbestos report

This sheet should be signed by all those carrying out work on the premises (including contractors, cleaners and staff). Persons signing this sheet are signing to say that they have seen the asbestos management plan and checked whether there is any known or presumed asbestos in the area in which they will be working.

If the contractor encounters suspected asbestos containing materials (ACM) that have not been previously identified they will immediately stop work, inform the Parish Council/Village Hall Caretaker and seek their further instructions.

| Date | Company name | Work being carried out/location on site | Name of person who has inspected the asbestos report | Signature |
| --- | --- | --- | --- | --- |